## Slide 1
Chapter 4 Network Layer
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved
The course notes are adapted for Bucknell’s CSCI 363
Xiannong Meng
Spring 2016

## Slide 2
4.1 introduction
4.2 virtual circuit and datagram networks
4.3 what’s inside a router
4.4 IP: Internet Protocol
  datagram format
  IPv4 addressing
  ICMP
  IPv6
4.5 routing algorithms
  link state
  distance vector
  hierarchical routing
4.6 routing in the Internet
  RIP
  OSPF
  BGP
4.7 broadcast and multicast routing
Chapter 4: outline

## Slide 3: Some examples of switchers, routers, and bridge
Linksys 48 port switch
(Wikipedia)
Back of a typical home router
(Wikipedia)
Cisco CRS-1 Core Router
(Wikipedia)

## Slide 4
Avaya ERS 2550T-PWR 50-port network switch
(Wikipedia)
Rack-mounted 24-port 3Com switch
(Wikipedia)
HP Procurve rack-mounted switches
mounted in a standard Telco Rack
19-inch rack with network cables
(Wikipedia)

## Slide 5: Router architecture overview
two key router functions:
run routing algorithms/protocol (RIP, OSPF, BGP)
forwarding datagrams from incoming to outgoing link
high-seed
switching
fabric
routing
processor
router input ports
router output ports
forwarding data plane (hardware)
routing, management
control plane (software)
forwarding tables computed,
pushed to input ports

## Slide 6: Input port functions
line
termination
link
layer
protocol
(receive)
lookup,
forwarding
queueing
decentralized switching:
given datagram dest., lookup output port using forwarding table in input port memory (“match plus action”)
goal: complete input port processing at ‘line speed’
queuing: if datagrams arrive faster than forwarding rate into switch fabric
physical layer:
bit-level reception
data link layer:
e.g., Ethernet
see chapter 5
switch
fabric

## Slide 7: Switching fabrics
transfer packet from input buffer to appropriate output buffer
switching rate: rate at which packets can be transfer from inputs to outputs
  often measured as multiple of input/output line rate
  N inputs: switching rate N times line rate desirable
three types of switching fabrics
memory
memory
bus
crossbar

## Slide 8: Switching via memory
first generation routers:
traditional computers with switching under direct control of CPU
packet copied to system’s memory
speed limited by memory bandwidth (2 bus crossings per datagram)
input
port
(e.g.,
Ethernet)
memory
output
port
(e.g.,
Ethernet)
system bus

## Slide 9: Switching via a bus
datagram from input port memory
to output port memory via a shared bus
bus contention: switching speed limited by bus bandwidth
32 Gbps bus, Cisco 5600: sufficient speed for access and enterprise routers
bus

## Slide 10: Switching via interconnection network
overcome bus bandwidth limitations
banyan networks, crossbar, other interconnection nets initially developed to connect processors in multiprocessor
advanced design: fragmenting datagram into fixed length cells, switch cells through the fabric.
Cisco 12000: switches 60 Gbps through the interconnection network
crossbar

## Slide 11
A 3-stage Banyan network switch logic
(n/2 log n) switching elements. In the
diagram, each node is a 2x2 switch. This
is a 16x16 switch (16 inputs and 16 outputs,
8 nodes, each with 2 inputs and 2 outputs.)
A cross-bar network switch logic
(nxn switching elements)
Images from Google

## Slide 12: Output ports
buffering required when datagrams arrive from fabric faster than the transmission rate
scheduling discipline chooses among queued datagrams for transmission
line
termination
link
layer
protocol
(send)
switch
fabric
datagram
buffer
queueing

## Slide 13: Output port queueing
buffering when arrival rate via switch exceeds output line speed
queueing (delay) and loss due to output port buffer overflow!
at t, packets move
from input to output
one packet time later
switch
fabric
switch
fabric

## Slide 14: How much buffering?
RFC 3439 (December 2002) rule of thumb: average buffering equal to “typical” RTT (say 250 msec) times link capacity C (RTT * C)
  e.g., C = 10 Gpbs link: 2.5 Gbit buffer
more recent (2004) recommendation: with N flows, buffering equal to
RTT C
.
N
http://yuba.stanford.edu/~nickm/papers/guido_buffer.pdf

## Slide 15: Input port queuing
fabric slower than input ports combined -> queueing may occur at input queues
  queueing delay and loss due to input buffer overflow!
Head-of-the-Line (HOL) blocking: queued datagram at front of queue prevents others in queue from moving forward
output port contention:
only one red datagram can be transferred. lower red packet is blocked
switch
fabric
one packet time later: green packet experiences HOL blocking
switch
fabric

## Slide 16: Queues, queues, and queues
The theory of queuing has significant applications and impact on the internet.
One of the pioneers of the internet, Leonard Kleinrock, is also known for his queuing systems book
  Kleinrock is a computer science professor at UCLA
  http://www.lk.cs.ucla.edu/index.html
  Queuing systems books
  http://www.amazon.com/Queueing-Systems-Volume-1-Theory/dp/0471491101

## Slide 17: Names, names, names
The naming of switchers, routers, and bridges can be confusing. In general, a switch implies that some or all ports have dedicated circuits; a router can forward traffic from input to output following certain algorithms (similar to switch) where ports may share circuits; a bridge interconnects different networks, some of which may run different protocols.
A device can be called a switch, a router, a routing switch, a bridge, or the like

## Slide 18: Devices with different protocol layers
Switches can run at different protocol layers
  Layer 2 switches use data link layer protocol (e.g., Ethernet)
  Layer 3 switches run network protocols (e.g., IPv4)
Routers typically run at data link layer (layer 2)
More specifics to come