## Slide 1
Chapter 5 Link Layer
Computer Networking: A Top Down Approach 6th edition Jim Kurose, Keith Ross Addison-Wesley March 2012
A note on the use of these ppt slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2012
J.F Kurose and K.W. Ross, All Rights Reserved
The course notes are adapted for Bucknell’s CSCI 363
Xiannong Meng
Spring 2016

## Slide 2: Link layer, LANs: outline
5.1 introduction, services
5.2 error detection, correction
5.3 multiple access protocols
5.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
5.5 link virtualization: MPLS
5.6 data center networking
5.7 a day in the life of a web request

## Slide 3: Multiprotocol label switching (MPLS)
initial goal: high-speed IP forwarding using fixed length label (instead of IP address)
  fast lookup using fixed length identifier (rather than shortest prefix matching)
  borrowing ideas from Virtual Circuit (VC) approach
  but IP datagram still keeps IP address!
S
TTL
PPP or Ethernet
header
IP header
remainder of link-layer frame
MPLS header
label
Exp
20
3
1
8
https://tools.ietf.org/html/rfc3031
MPLS
MPLS type
in E Type
0x8847: unicast
0x8848: multicast

## Slide 4: MPLS header and Ethernet header
http://www.gl.com/images/packetexpert-web-mpls-framing-format.gif

## Slide 5: MPLS capable routers
a.k.a. label-switched router
forward packets to outgoing interface based only on label value (don’t inspect IP address)
  MPLS forwarding table distinct from IP forwarding tables
flexibility: MPLS forwarding decisions can differ from those of IP
  use destination and source addresses to route flows to same destination differently (traffic engineering)
  re-route flows quickly if link fails: pre-computed backup paths (useful for VoIP)

## Slide 6: MPLS versus IP paths
R2
D
R3
R5
A
R6
IP router
IP routing: path to destination determined by destination address alone
R4

## Slide 7: MPLS versus IP paths
R2
D
R3
R4
R5
A
R6
IP-only
router
IP routing: path to destination determined by destination address alone
MPLS and
IP router
MPLS routing: path to destination can be based on source and dest. addr. and its resource requests.
  fast reroute: precompute backup routes in case of link failure
entry router (R4) can use different MPLS routes to A based, e.g., on source address

## Slide 8: MPLS signaling
modify OSPF, IS-IS link-state flooding protocols to carry info used by MPLS routing,
  e.g., link bandwidth, amount of “reserved” link bandwidth
entry MPLS router uses RSVP-TE signaling protocol to set up MPLS forwarding at downstream routers
D
R4
R5
A
R6
modified
link state
flooding
RSVP-TE
RSVP (ReSource reserVation Protocol) : http://tools.ietf.org/html/rfc2205
RSVP-TE (Traffic Engineering) : http://tools.ietf.org/html/rfc3209

## Slide 9: MPLS forwarding tables
R1
R2
D
R3
R4
R5
0
1
0
0
A
R6
in out out
label label dest interface
6 - A 0
in out out
label label dest interface
10 6 A 1
12 9 D 0
in out out
label label dest interface
10 A 0
12 D 0
1
in out out
label label dest interface
8 6 A 0
0
8 A 1
Router R4 can choose links reaching A
under MPLS

## Slide 10: Link layer, LANs: outline
5.1 introduction, services
5.2 error detection, correction
5.3 multiple access protocols
5.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
5.5 link virtualization: MPLS
5.6 data center networking
5.7 a day in the life of a web request

## Slide 11: Some Statistics About Google
June 2006 New York Times reported that Google’s Dalles, Oregan Data Center would create 60-120 full-time jobs
Rate of changes:
  March 2001, serving 70 million web pages with 8,000 computers
  In 2003, the number of computers grew to 100,000
  The June 2006 estimate was 450,000 scattered over at least 25 locations
  Jeff Dean’s presentation (~2009) anticipates 10 million computers in the next a few years
    Some anecdote https://plus.google.com/+JamesPearn/posts/VaQu9sNxJuY
    Jeff Dean on Google software architecture and large data center design ~2009

## Slide 12: A Few Other Google Data Centers (1)
Belgium Data Center:
  341 million dollars
  120 long-term jobs
  No chillers, just air-cooling, or called “free-cooling”
  Open early 2008
Lenoir, North Carolina Data Center
  600 million dollars
  150 acres
  200 long-term jobs

## Slide 13: A Few Other Google Data Centers (2)
Goose Creek, South Carolina Data Center
  600 million dollars
  520 acres
  200 jobs

## Slide 14: Google Data Center Information
Estimated (~2008) that Google has about 36 data centers world-wide
  Google maintains its data center temperature at 80 F
  Location map of Google data centers http://www.theregister.co.uk/2008/04/11/google_data_center_map/
  Google data center locations by Google (accessed 4/6/2016)
    https://www.google.com/about/datacenters/inside/locations/index.html
  Google data center video: http://www.youtube.com/watch?v=zRwPSFpLX8I
  Google data center FAQ: http://www.datacenterknowledge.com/archives/2012/05/15/google-data-center-faq/
See my lecture notes about overall Google system
  http://www.eg.bucknell.edu/~xmeng/webir-course/2014/lecture-notes-pdf/07-SearchEngine-Google.pdf

## Slide 15: Other Data Centers (Microsoft 1)
The Chicago Data Center:
  700,000 square feet – approximately the size of 16 football fields;
  Up to 220 shipping containers packed with servers; each container houses 1,800 to 2,500 servers, which makes 396,000 to 550,000 servers at the site! Each container can be wheeled in and out of the center in hours and be connected to the internet.
  Another source said a total capacity of 112 containers holding 224,000 servers.
  Go live July 20, 2009.

## Slide 16: Other Data Centers (Microsoft 2)
The Dublin Data Center (Ireland):
  303,000 square feet, first phase, eventually will reach 550,00 square feet
  Supported by 5.4 megawatts electricity.
  Go live on July 1, 2009. (Started in summer 2007.)
  500 million dollar project.
  Expected to create 250 jobs.

## Slide 17: Other Data Centers (Microsoft 3)
The Quincy Data Center (Washington):
  470,000 square feet room on a 75 acre site
  A tile floor and a maze of rooms centering around five 12,000-square-foot brain centers that contain tens of thousands of computer servers.
  Temperature kept in between 60 and 68 degree Fahrenheit
  Collects rainwater from its roof to use in its cooling system.
  Row after row of batteries to kick in for 18 seconds if a power failure should occur before the truck-sized backup generators fire up.
  Go live on March 27, 2007

## Slide 18: Other Data Centers (Microsoft 4)
The San Antonio Data Center (Texas):
  550 million dollar project
  470,000 square foot
  Two 10 megawatt utility feeds, each expandable to 30 megawatts each.

## Slide 19: Yahoo Data Center
Lockport, NY Data Center
  Using Niagara Fall as its power source
  150 million dollars
  30 acre site
  181,000 square feet rooms
  First phase : 10 megawatts of hydro-electric power; second phase another 15 megewatts
  To be completed by May 2010
Quincy, Washington Yahoo Data Center

## Slide 20: Data center networks
10’s to 100’s of thousands of hosts, often closely coupled, in close proximity:
  e-business (e.g., Amazon)
  content-servers (e.g., YouTube, Akamai, Apple, Microsoft)
  search engines, data mining (e.g., Google)
challenges:
  multiple applications, each serving massive numbers of clients
  managing/balancing load, avoiding processing, networking, data bottlenecks
Inside a 40-ft Microsoft container,
Chicago data center

## Slide 21: IP addresses and geolocations
IP addresses are not designed to have correlation with geo-locations;
However, software can collect the information using crowd-sourcing and report back;
Try
  http://www.iplocation.net/

## Slide 22
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
Load
balancer
Load
balancer
B
1
2
3
4
5
6
7
8
A
C
Border router
Access router
Internet
Data center networks
load balancer: application-layer routing
receives external client requests
directs workload within data center
returns results to external client (hiding data center internals from client)

## Slide 23
Server racks
TOR switches
Tier-1 switches
Tier-2 switches
1
2
3
4
5
6
7
8
Data center networks
rich interconnection among switches, racks:
  increased throughput between racks (multiple routing paths possible)
  increased reliability via redundancy

## Slide 24: Link layer, LANs: outline
5.1 introduction, services
5.2 error detection, correction
5.3 multiple access protocols
5.4 LANs
  addressing, ARP
  Ethernet
  switches
  VLANS
5.5 link virtualization: MPLS
5.6 data center networking
5.7 a day in the life of a web request

## Slide 25: Synthesis: a day in the life of a web request
journey down protocol stack complete!
  application, transport, network, link
putting-it-all-together: synthesis!
  goal: identify, review, understand protocols (at all layers) involved in seemingly simple scenario: requesting www page
  scenario: student attaches laptop to campus network, requests/receives www.google.com

## Slide 26: A day in the life: scenario
Comcast network
68.80.0.0/13
Google’s network
64.233.160.0/19
64.233.169.105
web server
DNS server
school network
68.80.2.0/24
web page
browser

## Slide 27: A day in the life… connecting to the Internet
router
(runs DHCP)
connecting laptop needs to get its own IP address, addr of first-hop router, addr of DNS server: use DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
DHCP request encapsulated in UDP, encapsulated in IP, encapsulated in 802.3 Ethernet
Ethernet frame broadcast (dest: FFFFFFFFFFFF) on LAN, received at router running DHCP server
Ethernet demuxed to IP demuxed, UDP demuxed to DHCP

## Slide 28: A day in the life… connecting to the Internet
router
(runs DHCP)
DHCP server formulates DHCP ACK containing client’s IP address, IP address of first-hop router for client, name & IP address of DNS server
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
UDP
IP
Eth
Phy
DHCP
DHCP
DHCP
DHCP
DHCP
encapsulation at DHCP server, frame forwarded (switch learning) through LAN, demultiplexing at client
Client now has IP address, knows name & addr of DNS
server, IP address of its first-hop router
DHCP client receives DHCP ACK reply

## Slide 29: A day in the life… ARP (before DNS, before HTTP)
router
(runs DHCP)
before sending HTTP request, need IP address of www.google.com: DNS
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS query created, encapsulated in UDP, encapsulated in IP, encapsulated in Eth. To send frame to router, need MAC address of router interface: ARP
ARP query broadcast, received by router, which replies with ARP reply giving MAC address of router interface
client now knows MAC address of first hop router, so can now send frame containing DNS query
ARP query
Eth
Phy
ARP
ARP
ARP reply

## Slide 30: A day in the life… using DNS
router
(runs DHCP)
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS
DNS
IP datagram containing DNS query forwarded via LAN switch from client to 1st hop router
IP datagram forwarded from campus network into comcast network, routed (tables created by RIP, OSPF, IS-IS and/or BGP routing protocols) to DNS server
demux’ed to DNS server
DNS server replies to client with IP address of www.google.com
Comcast network
68.80.0.0/13
DNS server
DNS
UDP
IP
Eth
Phy
DNS
DNS
DNS
DNS

## Slide 31: A day in the life…TCP connection carrying HTTP
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
to send HTTP request, client first opens TCP socket to web server
TCP SYN segment (step 1 in 3-way handshake) inter-domain routed to web server
TCP connection established!
64.233.169.105
web server
SYN
SYN
SYN
SYN
TCP
IP
Eth
Phy
SYN
SYN
SYN
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
SYNACK
web server responds with TCP SYNACK (step 2 in 3-way handshake)

## Slide 32: A day in the life… HTTP request/reply
router
(runs DHCP)
HTTP
TCP
IP
Eth
Phy
HTTP
HTTP request sent into TCP socket
IP datagram containing HTTP request routed to www.google.com
IP datagram containing HTTP reply routed back to client
64.233.169.105
web server
HTTP
TCP
IP
Eth
Phy
web server responds with HTTP reply (containing web page)
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
HTTP
web page finally (!!!) displayed

## Slide 33: Chapter 5: Summary
principles behind data link layer services:
  error detection, correction
  sharing a broadcast channel: multiple access
  link layer addressing
instantiation and implementation of various link layer technologies
  Ethernet
  switched LANS, VLANs
  virtualized networks as a link layer: MPLS
synthesis: a day in the life of a web request

## Slide 34: Chapter 5: let’s take a breath
journey down protocol stack complete (except PHY)
solid understanding of networking principles, practice
….. could stop here …. but lots of interesting topics!
  wireless
  multimedia
  security
  network management